## Slide 1: IoT architecture, protocoles
RT0911
Master Réseaux-Télécoms
Hacène Fouchal

## Slide 2: Contexte
Kevin Ashton a proposé le terme IoT en 1999.
Le concept : tout dispositif, tout capteur, tout logiciel dans tous les domaines sont interconnectés
Tout élément est accessible à distance
IoT= plateforme où des éléments sont connectés à Internet qui permettent une de collecter des données et de les échanger pour apprendre des autres (à l’image des humains).’

## Slide 3: Contexte

## Slide 4: Fonctionnement
Les dispositifs communiquent d’une façon sécurisée avec la plateforme IoT.
La platerfome IoT collete et combine les données venant de dispositifs et de plateformes et exécutent des analyses pour partager les informations les plus pertinentes pour répondre à une exigences applicative.

## Slide 5: Architecture IoT
illustration
Architecture IoT
Passerelles
Infrastructure Cloud
Infrastructure
réseau
Object

## Slide 6: Utilisation des IoT
5 domaines d’utilisation majeure des IoT :
  Intelligence artificielle : la technologie IoT rend les objets plus intelligents grâce aux données, aux réseaux et algorithmes
  Connectivité : devient opérationnelle pour des réseaux plus réduit dans mettre en cause l’efficacité
  Capteurs : donne la raison d’être des IoT.
  Interaction active entre éléments : Nouveau paradigme, on ajoute du service supplémentaire pour du contenu additionnel
  Dispositifs : sont plus réduits, plus puissants, moins chers qui montrent l’efficacité à grande échelle des IoT

## Slide 7: Historique-Perspectives

## Slide 8: Applications
Santé : le suivi médical pour des cas chronique apporte des solutions pour aussi bien ls malades que les médecins
Energie : la réduction de la consommation est cruciale
Education : Aide les formateurs à illustrer les idées. Le suivi en est plussimplifié.
Etatique : les « smart city » deviennent courantes partout pour gérer la mobilité, la gestion de l’énergie, des transports, …

## Slide 9: Architecture IoT

## Slide 10: Architecture IoT

## Slide 11: 4 composants IoT

## Slide 12: Exemple d’application de santé

## Slide 13: 1-Capteurs

## Slide 14: 2-Connectivité

## Slide 15: 3-Traitement des données

## Slide 16: 4-Interface Utilisateur

## Slide 17: Technologie IoT et Protocls
7 protocoles importants :
  Bluetooth
  Z-Wave
  Wifi
  Cellulaire
  NFC
  LoRaWan
  Zigbee

## Slide 18: Bluetooth

## Slide 19: Z-Wave

## Slide 20: wifi

## Slide 21: Cellulaire

## Slide 22: NFC

## Slide 23: LoRa Wan

## Slide 24: Zigbee

## Slide 25: Zigbee
ZigBee Alliance
  45+ companies: semiconductor mfrs, IP providers, OEMs, etc.
  Defining upper layers of protocol stack: from network to application, including application profiles
  First profiles published mid 2003
IEEE 802.15.4 Working Group
  Defining lower layers of protocol stack: MAC and PHY

## Slide 26: Caractéristiques
Data rates of 250 kbps , 20 kbps and 40kpbs.
Star or Peer-to-Peer operation.
Support for low latency devices.
CSMA-CA channel access.
Dynamic device addressing.
Fully handshaked protocol for transfer reliability.
Low power consumption.
Channels: 16 en 2.4Ghz ; 10 en 900Mhz ; 1 en 890Mhz
Extremely low duty-cycle (<0.1%)

## Slide 27: Caractéristiques
802.15.4 is a simple packet data protocol for lightweight wireless networks
  Channel Access is via Carrier Sense Multiple Access with collision avoidance and optional time slotting
  Message acknowledgement
  Optional beacon structure
  Target applications
    Long battery life, selectable latency for controllers, sensors, remote monitoring and portable electronics
  Configured for maximum battery life, has the potential to last as long as the shelf life of most batteries

## Slide 28: Types de dispositifs
There are two different device types :
  A full function device (FFD)
  A reduced function device (RFD)
The FFD can operate in three modes by serving as
  Device
  Coordinator
  PAN coordinator
The RFD can only serve as:
  Device

## Slide 29: Types de devices
Full function device (FFD)
  Any topology
  Network coordinator capable
  Talks to any other device
Reduced function device (RFD)
  Limited to star topology
  Cannot become a network coordinator
  Talks only to a network coordinator
  Very simple implementation

## Slide 30: En étoile
Full Function Device (FFD)
Reduced Function Device (RFD)
Communications Flow
Network
coordinator
Master/slave
Network
coordinator

## Slide 31: Pair à pair
Communications Flow
Full Function Device (FFD)
Point to point
Tree

## Slide 32: Couche Physique
PHY packet fields
  Preamble (32 bits) – synchronization
  Start of packet delimiter (8 bits) – shall be formatted as “11100101”
  PHY header (8 bits) –PSDU length
  PSDU (0 to 127 bytes) – data field

## Slide 33: Superframe
A superframe is divided into two parts
  Inactive: all station sleep
  Active:
    Active period will be divided into 16 slots
    16 slots can further divided into two parts
        Contention access period
        Contention free period

## Slide 34: Superframe
Beacons are used for
  starting superframes
  synchronizing with other devices
  announcing the existence of a PAN
  informing pending data in coordinators
In a “beacon-enabled” network,
  Devices use the slotted CAMA/CA mechanism to contend for the usage of channels
  FFDs which require fixed rates of transmissions can ask for guarantee time slots (GTS) from the coordinator

## Slide 35: Duty cycle
Each device will be active for 2-(BO-SO) portion of the time, and sleep for 1-2-(BO-SO) portion of the time

## Slide 36: Superframe
The structure of superframes is controlled by two parameters:
  beacon order (BO) : decides the length of a superframe
  superframe order (SO) : decides the length of the active potion in a superframe
For a beacon-enabled network, the setting of BO and SO should satisfy the relationship 0≦SO≦BO≦14
For channels 11 to 26, the length of a superframe can range from 15.36 msec to 215.7 sec (= 3.5 min).

## Slide 37: Slotted CSMA/CA algorithm
In slotted CSMA/CA
  The backoff period boundaries of every device in the PAN shall be aligned with the superframe slot boundaries of the PAN coordinator
    i.e. the start of first backoff period of each device is aligned with the start of the beacon transmission
  The MAC sublayer shall ensure that the PHY layer commences all of its transmissions on the boundary of a backoff period

## Slide 38: Slotted CSMA/CA algorithm (cont.)
Each device maintains 3 variables for each transmission attempt
  NB: number of times that backoff has been taken in this attempt (if exceeding macMaxCSMABackoff, the attempt fails)
  BE: the backoff exponent which is determined by NB
  CW: contention window length, the number of clear slots that must be seen after each backoff
    always set to 2 and count down to 0 if the channel is sensed to be clear
    The design is for some PHY parameters, which require 2 CCA for efficient channel usage.
Battery Life Extension:
  designed for very low-power operation, where a node only contends in the first 6 slots

## Slide 39: Slotted CSMA/CA (cont.)
need 2 CCA to ensure no collision

## Slide 40: Why 2 CCAs to Ensure Collision-Free
Each CCA occurs at the boundary of a backoff slot (= 20 symbols), and each CCA time = 8 symbols.
The standard species that a transmitter node performs the CCA twice in order to protect acknowledgment (ACK).
  When an ACK packet is expected, the receiver shall send it after a tACK time on the backoff boundary
    tACK varies from 12 to 31 symbols
  One-time CCA of a transmitter may potentially cause a collision between a newly-transmitted packet and an ACK packet.
  (See examples below)

## Slide 41: Why 2 CCAs (case 1)
Existing session
New transmitter
Backoff boundary
Backoff end here
CCA
CCA
Detect an ACK
New transmitter
Backoff end here
CCA
Detect an ACK

## Slide 42: Why 2 CCAs (Case 2)
Existing session
New transmitter
Backoff boundary
Backoff end here
CCA
Detect an DATA
New transmitter
Backoff end here
CCA
Detect an ACK

## Slide 43: Why 2 CCAs (Case 3)
Existing session
New transmitter
Backoff boundary
Backoff end here
CCA
Detect a DATA
New transmitter
Backoff end here
CCA
CCA
Detect an ACK

## Slide 44
Unslotted CSMA/CA
only one CCA

## Slide 45: GTS Concepts (I)
A guaranteed time slot (GTS) allows a device to operate on the channel within a portion of the superframe
A GTS shall only be allocated by the PAN coordinator
The PAN coordinator can allocated up to 7 GTSs at the same time
The PAN coordinator decides whether to allocate GTS based on:
  Requirements of the GTS request
  The current available capacity in the superframe

## Slide 46: GTS Concepts (II)
A GTS can be deallocated
  At any time at the discretion of the PAN coordinator or
  By the device that originally requested the GTS
A device that has been allocated a GTS may also operate in the CAP
A data frame transmitted in an allocated GTS shall use only short addressing

## Slide 47: GTS Concepts (III)
Before GTS starts, the GTS direction shall be specified as either transmit or receive
  Each device may request one transmit GTS and/or one receive GTS
A device shall only attempt to allocate and use a GTS if it is currently tracking the beacon
If a device loses synchronization with the PAN coordinator, all its GTS allocations shall be lost
The use of GTSs be an RFD is optional

## Slide 48: Association Procedures (1/2)
A device becomes a member of a PAN by associating with its coordinator
Procedures

## Slide 49: Association Procedures (2/2)
In IEEE 802.15.4, association results are announced in an indirect fashion.
  A coordinator responds to association requests by appending devices’ long addresses in beacon frames
Devices need to send a data request to the coordinator to acquire the association result
After associating to a coordinator, a device will be assigned a 16-bit short address.